## Slide 1
Interview Task:
Offshore Decommissioning
Presented by:
Karan Soni
Date : 22.11.2024
Place: Flensburg

## Slide 2
Index
Steps involved for Offshore Decommissioning
Factors Affecting Decommissioning
Vessels
My approach to Decommissioning Offshore Wind Farm
Flow chart of the code
Fuel Usage, CO2 Emissions, and Cost Analysis for Ships
Results
References

## Slide 3
1. Step involved on offshore Decommissioning
Decommissioning
Pre-Decommissioning
Decommissioning Operations
Post- Decommissioning
Reference: [1]

## Slide 4
1. Steps involved in Offshore Decommissioning
Figure 1.1: Traditional offshore turbine decommissioning options [1]
Figure 1.2: Offshore Wind turbine with Monopile Foundation [1]

## Slide 5
1. Step involved on offshore Decommissioning
Pre-Decommissioning
Decommissioning Strategy
Regulation
Financial Resources
Environmental Impact
partial removal
Advantages: Less cost, Less time consuming
Disadvantages: Environment risk such as trapping marine life. Maintenance and monitoring requirements
complete removal
Advantages: Minimizing long term rick, cleaner site for development new wind Farm
Disadvantages: High cost, longer duration.
Reference: [1]

## Slide 6
1. Step involved on offshore Decommissioning
Decommissioning Operation
Wind Turbines
Foundations
Offshore Substations
Cables
Lift
Cut and Lift
Onshore
Lift
Cut and Remove
Leave in situ
Substation Remove
Cable leave in situ

## Slide 7
1. Step involved on offshore Decommissioning
Post - Decommissioning
Handling of Removed Elements
Reuse
Recycle
Disposal
Monitoring and Maintainers
Surveys

## Slide 8
2. Factors Affecting Decommissioning
Foundation type
Vessel Availability
Distance to port
Water depth
Weather conditions
Time
CO2 Emission
Costs

## Slide 9
3. Vessels
Survey Vessel:
Fuel Type: HFO, Diesel, MGO, LNG, Methanol, Ammonia, Electricity
Size: Length: 80-100 m and Breadth: 15-18 m
Survey depth capacity: 2500 -3000 m [2] [3] [4] [5]
Figure 2.1: Survey Vessel [2]
2. SPIVs or Heavy Lift Vessel:
Fuel Type: HFO, Diesel, MGO, LNG, Methanol, Ammonia, Electricity
Size: Length: 220-382 meter and Breadth: 102-124 m
Lifting Capacity: 20000 -60000 tonnes [5] [6] [7]
Figure 2.2: Heavy Lift Vessel [6]

## Slide 10
3. Vessels
3. Support Vessel:
Dive support Vessel Offer a place to launch, supply, recover, to assist underwater
Crew boats Transferring person, environmental studies, support of shallow waters or the enforcement of safety zones
Workboats Cutting processes
Multicats Light transport, underwater support and stability handling
Tugs Normally they come with a small crane for stability handling.
Cargo barges Used for the transportation of components [1]

## Slide 11
4. My Approach to Decommissioning
Offshore Wind Farm
Pre-decommissioning
Decommissioning Strategy : Partial Remove Approach
Regulation, Financial resources: Right now, I assume, it is okay.
Environment Impact: Finding Co2 Emissions
Decommissioning Operation
Wind Turbine : 8 Wind Turbines (Assume 8MW one wind Turbine)
Turbine Type | Nacelle | Rotor blades | Tower
4 MW | 165 t | 20 t | 300 t
8 MW | 450 t | 35 t | 650 t
Table 4.1: Wind turbine components weight [1]

## Slide 12
4. My Approach to Decommissioning
Offshore Wind Farm
5. Foundation : Cut (Monopile Foundation)
6. Offshore substation, Cables Assuming Constant
Post-Decommissioning
Ignore it
Figure 4.1: Selected Decommissioning process for Wind Turbine [1]

## Slide 13
4. My Approach to Decommissioning
Offshore Wind Farm
Foundation type Monopile Foundation
availability Vessel Survey, SPIVs, Dive support, Crew boat, Work boat, Multicats, Cargo barges, Tugs
Distance to port 80km
Water depth 40 m
Weather conditions Normal
Time 4 [hours] + 15 days [assuming decommissioning per wind turbine] +
4.5 [hours]

## Slide 14
4. My Approach to Decommissioning
Offshore Wind Farm
Vessel | Fuel Consumptions ranges (litres/h) for Diesel | Port to Site | On Site | Site to Port
Survey | 200 - 300 | 250 | 200 | 250
SPIVs | 200 - 300 | 250 | 200 | 300
Dive support | 300 - 500 | 400 | 300 | 400
Crew boat | 100 - 200 | 150 | 100 | `150
Work boat | 200 -400 | 300 | 200 | 300
Multicats/ Tugs | 300 -500 | 400 | 300 | 400
Cargo | 500 - 1000 | 700 | 500 | 1000
Table 4.2: Vessel, Fuel Consumptions and case [6]

## Slide 15
4. My Approach to Decommissioning
Offshore Wind Farm
Vessel | Speed (km/h) / Travel Time = Dis./ speed | Port to Site | On Site | Site to Port
Survey | 18 -28 | 22 ( 3.63 hours) | - | 22
SPIVs | 18 - 28 | 22 | - | 18 (4.44 hours)
Dive support | 15 - 22 | 22 | - | 22
Crew boat | 28 - 37 | 28 (2.85 hours) | - | `28
Work boat | 15 - 23 | 22 | - | 22
Multicats | 15 - 22 | 22 | - | 22
Cargo | 18 - 27 | 22 | - | 18 (4.44 hours)
Table 4.3: Vessel, speed, travel time and case [6]

## Slide 16
4. My Approach to Decommissioning
Offshore Wind Farm
Case: Take to Wake
Fuel | Carbon Factor (gCo2/g Fuel) | Cost Energy [USD/kWh] | Energy Content (kWh/litres)
HFO | 3.114 | 0.043432836 | 9.6
Diesel | 3.206 | 0.06618267 | 10
MGO | 3.206 | 0.066 | 9.8
LNG | 2.750 | 0.0423 | 9
Methanol | 1.375 | 0.055175879 | 6
Ammonia | 0 | 0.123870968 | 4.5
Electricity | 0 | - | -
Table 4.4: Fuel types, carbon factor and cost [7]

## Slide 17
5. Flowchart of the code
+
Variable_Parameter.py
Case 1:
Consuming Fuel
Travelling time
Co2 Emission factor
Fuel density
Energy content
Energy Cost
Case 3:
Consuming Fuel
Travelling time
Case 2:
Consuming Fuel
Working time per day
Decommissioning wind turbine days
No of Wind turbine
Analysis.py
Start
Calculate Co2 emission and
Cost for different Fuel
Plot 1
Fuel Vs Co2 emission
Plot 2
Fuel Vs Cost
Stop
Start
Output.py
Case 1:
Calculate Co2 emission
Case 3:
Calculate Co2 emission
Case 2:
Calculate Co2 emission
Total Co2 emission
Plot
Stop
+
+
Code: https://github.com/KSoni1505/Fraunhofer_IWES_Interview_Task_Offshore-Decommissioning

## Slide 18
5. Flowchart of the code
Case 2:
Case 1 and Case 3:
Fuel Usage, CO2 Emissions, and Cost Analysis for Ships :
Emission = Amount of fuel [litres] * Density [g /litres] * Emission factor [g /g Fuel]
Fuel Cost [USD]= Amount of fuel [litres] * Energy content [kwh/litres] * Energy costs[USD/kwh]

## Slide 19
6. Fuel Usage, CO2 Emissions, and Cost Analysis for Ships
Figure 6.1: Energy Consumption Vs Co2 Emission [own drawing]
Figure 6.2: Energy Consumption Vs Cost [own drawing]

## Slide 20
7. Results
Figure 7.1: Vessel Types Vs Co2 emissions for different case [own drawing]

## Slide 21
7. Results
Figure 7.2: Script output [own Script]

## Slide 22
7. References
[1] Clara Ruiz,25.01.2019. “Decommissioning of offshore Wind turbine” Escola de Camins. TFG_Decommissioning_Clara Ruiz.pdf, 15.11.2024.
[2] Fugro, Creating a Safe and Liveable World | | Fugro , 15.11.2024.
[3] Geoquip Elena, Geoquip Elena + Deep-Push Cpt | Geoquip Marine, 15.11.2024.
[4] Edda Wind, Home - Edda Wind, 15.11.2024.
[5] Taken data from present work, rasant, 15.11.2024.
[6] Nunzia Capobianco - Vincenzo Basile - Francesca Loia Roberto Vona, 27.July.2022. ”End-of-life management of oil and gas offshore platforms: challenges and opportunities for sustainable decommissioning.” 14-capobianco-et-al.-118-2022.pdf, 17.11.2024.
[7] Briefing, March,2021. https://theicct.org/wp-content/uploads/2021/06/Well-to-wake-co2-mar2021-2.pdf 15.11.2024.